## Slide 1: GARRISON Dam Spillway Modification PRoject
Omaha District
Jeff Greenwald – Project Manager

## Slide 2: Project overview

## Slide 3
Garrison Dam and Project Location
Garrison Dam
Cottonwood Creek Dam
North Dakota

## Slide 4: Garrison Dam and Project Overview
Project Authorization:
  The Garrison Dam - Lake Sakakawea Project was authorized by the Flood Control Act (approved 22 December 1944) as part of the general comprehensive plan for flood control and other purposes in the Missouri River Basin.
The authorized purposes include:
  Flood risk management
  Hydroelectric power
  Water supply
  Water quality control
  Irrigation
  Recreation
  Navigation
  Fish and wildlife

## Slide 5: Garrison Dam cost-sharing
The Western Area Power Administration (WAPA) is responsible for marketing and transmitting power and are assessed a portion (43.78%) of any joint activities, dam safety included, for repayment to the treasury.
More favorable cost-sharing applied based on:
  Section 1203 of WRDA 1986.
  Section 1139 of WRDA 2016.
  Special cost-sharing for modifications to dams resulting from new hydrologic or seismic data or changes in state-of-the-art design criteria.
The recently completed Dam Safety Modification Study (DSMS) requested a reduced cost-share from ASA(CW) for WAPA because the modifications are needed based on new hydrologic data and changes in state-of-the-art design.
Cost-share reduction could result in WAPA share reduction to ~7% from 43.78% of project costs.

## Slide 6
Reservoir Capacity Overview
  Garrison Dam (largest Mainstem dam).
  Largest reservoir operated by USACE.
  Third largest reservoir in the U.S.
  Garrison total capacity.
  23.5 MAF (top of flood pool).
  34.4 MAF (top of dam).
  19.4 MAF (current pool)*

## Slide 7: Garrison Dam
Length of dam: 11,300 ft (including spillway)
Maximum height: 210 ft
Embankment fill: 66,500,000 cy
Length of reservoir: 178 miles (1340 miles shoreline)
Proposed modifications focused on spillway
Notes: This aerial photo looking back to the north shows Lake Sakakawea impounded behind the dam. The reservoir at maximum pool would extend upstream approximately 178 miles. The dam is over 11,000 feet long with the spillway located on the left abutment (photo right) and the powerhouse/outlet works is located on the right abutment (photo left). The dam has a maximum height of 210 feet. The proposed modifications are focused on addressing risk driving potential failure modes in the spillway.

## Slide 8: Garrison Dam Project Features
8
Project Office (Riverdale)
Spillway Bridge
Main Embankment
(66.5M CY)
Maintenance Facility
Former Pilot Channel
Lake Sakakawea
Missouri River
Former River Channel
Relief Well Channel
Intake Structure
Crest Road
(Highway 200)
Tailrace
Powerhouse
Cut Slopes
Spillway Chute
Switchyard
Regulatory Tunnels
Powerhouse
Spillway Stilling Basin

## Slide 9: Project Features SPILLWAY
Crest Structure
  28 Tainter gates (40’ x 29’)
  Top of Gates EL 1854 ft LPD
  Gated Ogee Weir crest EL 1825 ft LPD
  Width – 1,336 feet (including piers)
Upper chute – 0.75% slope, converges to 800 ft width
Lower chute – 20% slope
Stilling basin – 200 ft long with baffle blocks and end sill
Design Discharge Capacity 827,000 cfs EL 1859 ft LPD
Flow
Upper
Chute
Lower
Chute
Stilling
Basin
Approach Channel
Spillway Bridge

## Slide 10: Dam safety risks

## Slide 11
  ROUTINE DAM SAFETY PROGRAM
Every 10 Years
  PERIODIC ASSESSMENT
Potential Deficiency Identified Requiring Further Evaluation
  ISSUE EVALUATION STUDY
Issue Confirmed to Warrant Further Action
  DAM SAFETY MODIFICATION STUDY
Selection of Alternatives to Reduce Risk to an Acceptable Level
  PLANNING, ENGINEERING, AND DESIGN
Construction
How does the corps Manage Risk?
  U.S. Army Corps of Engineers risk management process:
Potential Deficiency Identified Requiring Further Evaluation
We are here
Public Safety is the #1 Priority in the Corps Dam Safety Program

## Slide 12: Garrison Dam Risk Assessment Timeline
  Screening for Portfolio Risk Analysis (SPRA) in 2006 resulted in Dam Safety Action Classification (DSAC) 4 rating.
  2011 record system runoff/inflows, inaugural spillway flow.
  Detailed visual, physical, and geophysical assessment of chute slab and stilling basin.
  Comprehensive inspection of the spillway underdrains.
  Inspection and evaluation of the west abutment and west terrace underseepage control features.
  Poor performance of drainage system observed during spillway discharges (manhole covers removed resulting in pressurized drainage system and damaged subdrain pipe)
  2013 Periodic Assessment.
  Reclassified to DSAC 2 primarily due to severity of incremental consequences.
  2016 Issue Evaluation Study (IES).
  Findings confirmed there are dam safety risk concerns.
  DSAC 2 classification confirmed/upheld in April 2020.
  PMF Updated – increased peak pool and spillway discharge (reasonable high PMF). 1.15M cfs at El. 1871.4 feet LPD.
  2020-2023 Dam Safety Modification Study (DSMS).
  July 2023 – Start of Preconstruction Engineering & Design (PED).
2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023
2011 Flood Event, Inaugural Spillway Flow
June-Aug 2011
PA
Jun 2013
DSAC 2
Apr 2015
IES
Apr 2016
SPRA
May 2006
DSAC 4
Dec 2008
DSMS
Aug 2020
DSMS Complete
May 2023
2011 - Emergency repairs conducted after initial release of ~30,000 cfs, prior to peak release of ~60,000 cfs
PED
June 2023
DSMS = Dam Safety Modification Study
PED = Preconstruction Engineering and Design
DSAC = Dam Safety Action Classification
IES = Issue Evaluation Study
PMF = Probable Maximum Flood
PFM = Potential Failure Mode
RMP = Risk Management Plan

## Slide 13: Why are we here: Address Dam Safety Risks
  Recommended Plan for Modification for Pre-Construction Engineering and Design (PED) Phase
  Structural modifications to crest structure, spillway gate retrofits, a new concrete overlay on top of existing slab, drainage system replacement, armoring areas outside/adjacent to chute walls, and stilling basin improvements.
    Modified spillway will be able to safely pass new PMF
  Smaller scope items:
    New spillway gate deicing system and intervention measures.
    New line of subdrains on west abutment above powerplant (small-scope item, likely separate contract from spillway work)
  Significant life safety risk exists at Garrison Dam (i.e., Risks that are not tolerable)
    DSAC 2 – High Risk. Six actionable spillway failure modes
    Consequences of uncontrolled release are very significant
    Issues associated with existing drainage system confirmed after 2011 releases
    Issues associated with hydraulic performance after Probable Maximum Flood (PMF) increased ~40%.
    Overtopping issues/stilling basin stability issues.
2011 Flood Control Releases
Notes: This is a dam safety project. The project is a DSAC 2. There are six actionable failure modes in the spillway and the consequences of a failure are very high.
In 2011 when the spillway was operated for flood control for the first time there were issues with the drainage system identified. Lost two manholes of 27 in spillway chute.
  Two of the actional failure modes related to drainage system.
USACE conducted multiple risk assessments leading up to the mod study after that. The PMF was updated which resulted in a 40% increase in the maximum spillway discharge.
  Four of the actional failure modes related to the increases in hydraulic loading.

## Slide 14
PFM 37 – Spillway gate failure
Hydraulic Jump
PFM 8 – Hydraulic jacking of the lower spillway chute and stilling basin slab due to uplift
PFM 7 – Hydraulic jacking of chute slab due to manholes
PFM 7C – Hydraulic jacking of chute slab due to drain defects
Spillway Risk Driving Potential Failure Modes
PFM 42 – Overtopping of spillway chute walls (PFM 42)
PFM 41 – Overtopping of spillway abutment monoliths

## Slide 15: Spillway drain concerns (PFM 7 and 7C)
Open spillway manholes would allow flow into drainage system (over-pressurize)
Damaged drain-pipe allows frost blanket material into drain
Void under slabs could become large enough to cause collapse, exposing end of slab to high velocities
Manhole cover removed during spillway releases - 2011
Typ. spillway manhole covers
Drain Defects

## Slide 16: Lower spillway chute and stilling basin uplift concern (PFM 8)
Hydraulic Jump
Existing lignite layers exacerbate the potential for undesirable hydraulic pressures during high flows.
These hydraulic pressures can result in enough force on the bottom of the spillway concrete in the lower chute to heave a slab.
Notes: The next slide talks about the lower spillway chute and stilling basin uplift concerns:
The existing lignite layers exacerbate the potential for undesirable hydraulic pressures under the SB slab during high flows. This is due to these lignite layers being hydraulically connected to the d/s TW pool; which can be up to 80 feet during design events.
These hydraulic pressures can result in enough force on the bottom of the spillway concrete in the lower chute to heave a slab.

## Slide 17: Overtopping of spillway chute walls concern (PFM 42)

## Slide 18: Overtopping of spillway abutment monoliths concern (PFM 41)
Looking downstream
Looking upstream
New peak pool elevation would result in overtopping of the abutment monoliths at elevation 1862 LPD.
Could result in scour downstream of monolith.

## Slide 19: Spillway gate failure concern (PFM 37)
New maximum pool elevation would overtop the Tainter gates.
The connection of the gates to the piers would be overstressed and could fail.
Upstream side of Tainter gate
Image of crest structure with potential failure point circled in red
Downstream side of gate and trunnion hub

## Slide 20: proposed modifications and Schedule

## Slide 21
Hydraulic Jump
Measure 8-1
RCC overlay with concrete cap (from 2.5 ft up to 16 ft thick)
(Addresses PFM 8 – Hydraulic jacking of the lower spillway chute and stilling basin slab due to uplift)
Recommended Plan
Measures 37-1, 37-4
Trunnion hub modifications and construct concrete wall/beam between piers to deflect nappe, reduce load on gates
(Addresses PFM 37 – Spillway gate failure)
Measure 42-2
Armor entire area behind walls
(Addresses PFM 42 – Overtopping of spillway chute walls)
Measure 41-1
Seal abutment monoliths
(Addresses PFM 41 – Overtopping of spillway abutment monoliths)
Measures 7-4, 7C-3
Replace drainage pipes, abandon old VCP pipe network, 2.5’ CRC overlay
(Addresses PFM 7 – Hydraulic jacking of chute slab due to manholes and PFM 7C – Hydraulic jacking of chute slab due to drain defects)
Minor features not shown: The recommended plan also includes a new line of drains on the west abutment and new spillway gate deicing features.

## Slide 22: PED Schedule
Jan 2026. 35% Design Complete.
Fall 2026. Integrated Design and Construction Contract Award.
Mar 2028. 65% Design Complete.
Feb 2029. 95% Design Complete.
Aug 2029. 100% Design Complete.
2029 – 2035. Anticipated Construction Duration.
*Proposed dates are approximate and subject to change*

## Slide 23: Questions

## Slide 24
RECOMMENDED PLAN OVERVIEW
G-02
# | LOCATION | TASK
1 | UPPER CHUTE & UPSTREAM HALF OF LOWER CHUTE - DRAINS, Sta 40+00 to 63+00 | DRAINAGE REPLACEMENT, CRC OVERLAY
2 | DOWNSTREAM HALF OF LOWER CHUTE AND STILLING BASIN, Sta 63+00 to 69+00 | OVERLAY (RCC WITH CRC CAP), LARGER BAFFLE BLOCKS MOVED DOWNSTREAM, LARGER END SILL
3 | CHUTE WALLS | ARMOR BEHIND CHUTE WALLS
4 | ABUTMENT MONOLITHS | SEAL SPILLWAY ABUTMENTS
5 | SPILLWAY GATES | CONSTRUCT BEAMS TO DEFLECT NAPPE, TRUNNION HUB MODIFICATIONS
REPLACE DRAINAGE SYSTEM, CHUTE OVERLAY, ARMOR BEHIND CHUTE WALLS, DEFLECT NAPPE FROM GATES, MODIFY TRUNNION HUB
CONSTRUCT DEFLECTOR BEAMS BETWEEN PIERS TO DEFLECT NAPPE, MODIFY TRUNNION HUB CONNECTIONS
TYPICAL TW EL 1670
SLAB EL 1802
WEIR EL 1825
ACCESS SHAFTS
STILLING BASIN EL 1620
1 2 3
20% SLOPE
TOP OF WALL
NEW COLLECTOR GALLERY
0.75% SLOPE
NEW COLLECTOR GALLERY
ABANDON EXISTING DRAINS
NEW
LATERAL
DRAINS
REPLACE RELIEF WELL DRAINS
63+00
500 ft
RETAIN EXISTING DRAINS
STA 45+00
STA 40+00
STA 50+00
STA 55+00
STA 60+00
STA 63+00
STA 69+00
SEAL MONOLITHS 31 - 33
SEAL MONOLITHS 1 - 3
OVERLAY (UP TO 16 FT THICK); NEW, LARGER BAFFLES; LARGER END SILL
OVERLAY
NOTE- DOWNSTREAM NEW LATERALS TO BE CO-LOCATED WITH EXISTING LINES 8 AND 9. SHOWN OFFSET HERE FOR CLARITY.
OVERLAY (2.5 FT CRC)
CONCRETE ARMOR BEHIND CHUTE WALLS
4 ACCESS
MANHOLES
PER GALLERY